## Slide 1: 2026.03.05 일일 보고 학습 내용 정리
공민수 석사과정생

## Slide 2: 목차
Pole Placement PI & DOB
  Tracking Performance with Bode plot
  Disturbance Estimation Performance
Adding Feed Forward Control
  Change of Control Input & Tracking Performance
Adding the nominal values of maxon motor
  Effect of Saturation

## Slide 3: Pole Placement PI & DOB 구현
Velocity Control Block Diagram with PI & DOB
Arbitrary Constant Parameters
Varying Parameters
  Frequency of Reference
  Frequency of Disturbance
J | B | zeta | wn | Bandwidth | Magnitude Reference | Magnitude Disturbance | LPF Cutoff Fq
1[ ] | 0.5[] | 0.7 | 10[rad/s] | 1.59[Hz] | 10[rad/s] | 10[] | 10[]
J | B | zeta | wn | Bandwidth | Magnitude Reference | Magnitude Disturbance | LPF Cutoff Fq
 |  | 0.7 | 10[rad/s] | 1.59[Hz] | 10[rad/s] |  | 

## Slide 4: Tracking Performance with Bode plot
Approach
  Relationship between Reference frequency and PI Bandwidth
Analysis Method
  Tracking Performance Observation by Adjusting Input Frequency Based on Bode Plot Gain and Phase
Gain = 1.1995
Magnitude = 1.58 [dB]
Phase = -36.57 [deg]
Wn

## Slide 5: Tracking Performance with Bode plot
Results
  Frequency of reference = Bandwidth
Output Peak = 12.02 [rad/s]
Reference peak = 10 [rad/s]
Gain = 1.202
Phase Delay = 0.061 [s]
Frequency= 1.59 [Hz]
Phase = 34.91 [deg]
Time [s]
W[rad/s]
W[rad/s]
Time [s]
Ref
Output

## Slide 6: Tracking Performance with Bode plot
Conclusions
  The bandwidth in pole placement can be used to tune the frequency range for tracking.
  Frequency of reference > >Bandwidth
Results
  Frequency of reference << Bandwidth
Time [s]
W[rad/s]
W[rad/s]
Time [s]
Ref
Output

## Slide 7: Disturbance Estimation Performance
Approach
  Relationship between Reference frequency and PI Bandwidth
Analysis Method
  Estimation Performance by Adjusting Disturbance Frequency Based on 1st LPF
Results
Conclusion
  The Disturbance estimation performance is influenced by the cutoff frequency of the LPF
Time [s]
W[rad/s]
1[Hz]
5[Hz]
10[Hz]
D_hat
D

## Slide 8: Adding Feed Forward Control
Velocity Control Block Diagram with PI, DOB & Feed Forward
Parameters is the Same with ‘Velocity output with PI & DOB’ and Feed Forward Cutoff Frquency is 150 [Hz]

## Slide 9: Change of Control Input & Tracking Performance
Change of Control Input Upi, Udob, Uff respectively
  Upi & Udob
  Upi & Udob & Uff
-20 < Upi < 20 []
-10 < Udob < 10 []
-30 < Utotal < 30 []
-2 < Upi < 2 []
-10 < Udob < 10 []
-20 < Uff < 20 []
-30 < Utotal < 30 []
Upi
Udob
Uff
Time [s]
Time [s]
T[Nm]
T[Nm]

## Slide 10: Change of Control Input & Tracking Performance
Change of the Tracking Performance
  Upi & Udob
  Upi & Udob & Uff
Phase lag and Tracking Error
Good Error and response performance
Ref
Output
Ref
Output
Time [s]
Time [s]
W[rad/s]
W[rad/s]

## Slide 11: Adding the nominal values of maxon motor
Velocity Control Block Diagram with PI, DOB & Feed Forward (Maxon motor)
Nominal Parameters
Jn | Bn | Saturation(Rated Torque)
[ ] | [] | []
Jn | Bn | Saturation(Rated Torque)

## Slide 12: Effect of Saturation
Analysis
  Saturation case’s Upi is bigger than Ideal Case
  Saturation case’s Udob becomes irregular than Ideal Case
  Saturation Case
Change of Control input
  Ideal Case
Time [s]
Time [s]
T[Nm]
T[Nm]
Upi
Udob
Uff

## Slide 13: Effect of Saturation
Analysis
  Phase Lag, Magnitude Decrease
Conclusion
  Actuator saturation leads to error accumulation, which increases the integrator output and degrades the tracking performance.
  Saturation Case
Reference Tracking Performance
  Ideal Case
Time [s]
W[rad/s]
W[rad/s]
Time [s]
Ref
Output

## Slide 14: TO DO
Rover wheel을 통해 시뮬레이션으로 학습했던 내용들을 실습해본다.
특히 입력 주파수 대역과 Bandwidth, Cutoff Frequency를 고려하며 tracking튜닝을 진행한다.